SECTION 09800

www.gsacoustics.com

Reflections Ceiling Reflectors

ACOUSTICAL TREATMENT

** NOTE TO SPECIFIER **  Golterman & Sabo; acoustical wall panels, ceiling products, sound diffusers and reflectors.

.

This section is based on the products of Golterman & Sabo, which is located at:

3555 Scarlet Oak Boulevard

St. Louis, MO  63122

Tel:  (800) 737-0307

Tel: (636) 225-8800

Fax: (636) 225-2966

Email: inquiry@golterman.com

www.golterman.com

.

Golterman & Sabo makes a wide variety of acoustical control products. In addition to wall and ceiling panels, banners, and suspended "clouds" that are used for sound absorption, they also produce wall and ceiling sound diffusers and sound reflectors.

.

SECTION 09800 - ACOUSTICAL TREATMENT, Copyright 2002, ARCAT, Inc.

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Ceiling Reflector Panel. Work Included: Provide Golterman & Sabo Reflections Ceiling Reflector, where shown on Architectural Drawings, and as specified in this Specification.

QUALITY ASSURANCE

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Golterman & Sabo’s Reflections Ceiling Reflector Products for this project shall maintain the quality as instituted by the architect or Golterman & Sabo.

Design Criteria: Manufacture of Reflections Panels shall be installed true and plumb to within manufacturing tolerance of 1/8” over 8’ long

Product Construction: Thermoformed copolymer sheets

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

ASTM C 423 - Standard Test Method for Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method; 2000.

ASTM E 84 - Standard Test Method for Surface Burning Characteristics of Building Materials; 2000a.

PERFORMANCE REQUIREMENTS

** NOTE TO SPECIFIER **  Delete the following paragraph if only tackable panels are specified.

Acoustical Absorption:  Perform testing in accordance with ASTM C 423,

Flame Spread Rating:  Provide all components with Class A flame spread rating when tested in accordance with ASTM E 84, unless otherwise specified.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Independent testing agency test reports.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each product specified, two complete sets of color samples representing manufacturer's full range of available colors and patterns.

QUALITY ASSURANCE

Manufacturer Qualifications:  Minimum 10 years of experience in producing acoustical products of the types specified herein.

Installer Qualifications:  Acceptable to the manufacturer of the acoustical products being installed.

** NOTE TO SPECIFIER **  Include a mock-up if the project size and/or quality warrant taking such a precaution.  The following is one example of how a mock-up on a large project might be specified.  When deciding on the extent of the mock-up, consider all the major different types of work on the project.

Mock-Up:  Provide a mock-up for evaluation of installed appearance.

Install acoustical products in areas designated by Architect.

Do not proceed with remaining work until Architect approves workmanship and appearance.

Approved mock-up may remain as part of the work.

DELIVERY, STORAGE, AND HANDLING

Protect acoustical products from moisture during shipment, storage, and handling.

Store products in manufacturer's unopened packaging until ready for installation.

Store materials flat, in dry, well-ventilated space.

Do not stand panels on end.

Protect edges from damage.

Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

PROJECT CONDITIONS

Do not begin installation of acoustical products until building has been enclosed and environmental conditions approximate those that will prevail when building is occupied.

Environmental Requirements:  Do not install panels until wet work, such as concrete and plastering, is complete; the building is enclosed; and the temperature and relative humidity are stabilized at 60 – 80 degrees F (16 – 27 degrees C) and 40% to 50%, respectively.

EXTRA MATERIALS

** NOTE TO SPECIFIER **  Include this article if the project size and/or quality warrant the additional expense and the Owner has adequate storage space available for this purpose.  The following is one example of how extra materials on a large project might be specified.  Edit the percentage as appropriate for the project, or change the text to require a specific number.

See Section 01600 - Product Requirements, for additional provisions.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  G&S Acoustics; 3555 Scarlet Oak Blvd., St. Louis, MO  63122.    Tel:  (636) 225-8800 or (800) 737-0307.  Fax:  (636) 225-2966. Email:  inquiry@gsacoustics.com.  www.gsacoustics.com.

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

Provide all acoustical products specified herein by a single manufacturer.

CEILING REFLECTOR

** NOTE TO SPECIFIER **  Delete all product types not required; under each product type retained, delete options not required. If more than one combination of features is required; edit to indicate where each combination is to be used.

Ceiling Reflectors: Reflections Ceiling Reflectors; thermoformed copolymer ceiling reflector with properties as follows:

Reflections – Standard: 0.125” thermoformed copolymer.

Reflections – Low Frequency Absorption: 0.125” thermoformed copolymer laminated with 2 inches (51mm), 1.5pcf (24 kg/cu m) sound absorbing glass matting.

Size: As indicated on drawings, max size 4’x8’.

Custom sizes available upon request.

Finish: Standard white textured finish.

Finish: Custom colors available.

Finish: Fabric-Wrapped, color as selected from manufacturer’s standards.

Mounting: Internal aluminum frame.

** NOTE TO SPECIFIER **  Delete all but one thickness below.  If more than one is required, edit headings to indicate where each is to be used.

** NOTE TO SPECIFIER **  Delete two of the following three paragraphs.  Custom sizes and shapes up to 4 by 12 ft and 5 by 10 ft are available.

EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

The contractor shall measure ceiling areas and establish layout for hangers and carriers, in accordance with installation instructions.

The Reflections panels shall be handled and installed with care in order to prevent surface and structure damage.

The contractor shall suspend panels in accordance with manufacturers recommended installation guides and shop drawings. “Unistrut” supporting members are a contractor supplied item and shall be suspended according to architect’s drawings and manufacturers’ shop drawings.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

WARRANTY

All materials supplied by Golterman & Sabo shall be guaranteed against manufacturing defects for one year.

The contractor shall warranty for one year all work from final acceptance of completed work.

END OF SECTION